## Slide 1: Lists, arrays, functions, tables and plots
MODULE 02 · LESSON 2 OF 4 · ≈ 10 MIN
Module 2: Python and Jupyter foundations
The data structures you will use
2.2
Notes: Welcome to Module 2, Lesson 2 of the self-paced course Machine Learning Fundamentals for Surrogate-Based Engineering Optimization: Lists, arrays, functions, tables and plots. This lesson belongs to the module Python and Jupyter foundations and takes about 10 minutes. In this lesson: The data structures you will use.

## Slide 2: The data structures you will use
Lesson 2 · Lists, arrays, functions, tables and plots · Intuition
A Python list is an ordered collection: [0.8, 1.2, 1.6]. A NumPy array is a fast, numerical grid supporting element-wise arithmetic: s * 1e-3 converts every value to metres at once. A pandas DataFrame is a table with named columns. A function packages a calculation so it can be reused: heat_sink(s_mm, t_mm).
Shapes of a 1-D array (n,), a 2-D feature array (n, d), a target vector, and a pandas table.
Notes: The data structures you will use. A Python list is an ordered collection: [0.8, 1.2, 1.6]. A NumPy array is a fast, numerical grid supporting element-wise arithmetic: s * 1e-3 converts every value to metres at once. A pandas DataFrame is a table with named columns. A function packages a calculation so it can be reused: heat_sink(s_mm, t_mm). Look at the figure. Shapes of a 1-D array (n,), a 2-D feature array (n, d), a target vector, and a pandas table. Five cells in a row labelled 1-D array shape (5,); a 5 by 2 grid labelled 2-D array X shape (5, 2) rows are samples; a 5 by 1 column labelled target y; and a small table with columns s_mm, t_mm, R_KperW.

## Slide 3: The data structures you will use
Lesson 2 · Lists, arrays, functions, tables and plots · The mathematics (1/2)
Array shape is written (rows, columns). scikit-learn expects features X with shape (n, d) and targets y with shape (n,).
import numpy as np
import pandas as pd
import matplotlib.pyplot as plt
s = np.array([0.8, 1.2, 1.6, 2.0, 2.4, 2.8]) # fin gaps, mm (1-D array, shape (6,))
t = np.full_like(s, 0.6) # same thickness for all, mm
X = np.column_stack([s, t]) # 2-D array, shape (6, 2)
df = pd.DataFrame({"s_mm": s, "t_mm": t}) # table with named columns
print(X.shape, df.shape)
df.head()
Notes: Now the mathematics. Array shape is written (rows, columns). scikit-learn expects features X with shape (n, d) and targets y with shape (n,). (The code listing is shown on the slide: import numpy as np; import pandas as pd; import matplotlib.pyplot as plt; s = np.array([0.8, 1.2, 1.6, 2.0, 2.4, 2.8]) # fin gaps, mm (1-D array, shape (6,)); t = np.full_like(s, 0.6) # same thickness for all, mm; X = np.column_stack([s, t]) # 2-D array, shape (6, 2); df = pd.DataFrame({"s_mm": s, "t_mm": t}) # table with named columns; print(X.shape, df.shape); df.head())

## Slide 4: The data structures you will use
Lesson 2 · Lists, arrays, functions, tables and plots · The mathematics (2/2)
A function bundles the heat-sink model (this exact code appears in every lab):
def heat_sink(s_mm, t_mm):
"""Pedagogical plate-fin heat-sink model. Inputs in mm.
Returns thermal resistance R (K/W), mass (kg) and air temperature rise (K)."""
W, L, H, tb = 0.050, 0.050, 0.040, 0.004 # m
ks, rho_al = 150.0, 2700.0 # W/(m K), kg/m^3
rho, mu, cp, ka = 1.16, 1.85e-5, 1007.0, 0.026 # air properties
dp, Q, Nu = 5.0, 30.0, 7.54 # Pa, W, -
s, t = s_mm * 1e-3, t_mm * 1e-3 # mm -> m (check units!)
N = W / (s + t)
u = dp * s**2 / (12 * mu * L)
mdot = rho * u * s * H * N
h = Nu * ka / (2 * s)
m = np.sqrt(2 * h / (ks * t))
eta = np.tanh(m * H) / (m * H)
UA = h * N * L * (2 * H * eta + s)
NTU = UA / (mdot * cp)
R = 1 / (mdot * cp * (1 - np.exp(-NTU))) + tb / (ks * W * L)
mass = rho_al * (N * t * H * L + W * L * tb)
dT_air = Q / (mdot * cp)
return {"R": R, "mass": mass, "dT_air": dT_air}
print(heat_sink(2.0, 0.8))
Notes: Continuing. A function bundles the heat-sink model (this exact code appears in every lab): (The code listing is shown on the slide: def heat_sink(s_mm, t_mm):; """Pedagogical plate-fin heat-sink model. Inputs in mm.; Returns thermal resistance R (K/W), mass (kg) and air temperature rise (K)."""; W, L, H, tb = 0.050, 0.050, 0.040, 0.004 # m; ks, rho_al = 150.0, 2700.0 # W/(m K), kg/m^3; rho, mu, cp, ka = 1.16, 1.85e-5, 1007.0, 0.026 # air properties; dp, Q, Nu = 5.0, 30.0, 7.54 # Pa, W, -; s, t = s_mm * 1e-3, t_mm * 1e-3 # mm -> m (check units!); N = W / (s + t); u = dp * s**2 / (12 * mu * L); mdot = rho * u * s * H * N; h = Nu * ka / (2 * s); m = np.sqrt(2 * h / (ks * t)); eta = np.tanh(m * H) / (m * H); UA = h * N * L * (2 * H * eta + s); NTU = UA / (mdot * cp); R = 1 / (mdot * cp * (1 - np.exp(-NTU))) + tb / (ks * W * L); mass = rho_al * (N * t * H * L + W * L * tb); dT_air = Q / (mdot * cp); return {"R": R, "mass": mass, "dT_air": dT_air}; print(heat_sink(2.0, 0.8)))

## Slide 5: The data structures you will use
Lesson 2 · Lists, arrays, functions, tables and plots · In engineering practice
Engineering application
Because heat_sink uses NumPy operations, it accepts arrays: heat_sink(np.array([1.0, 2.0]), np.array([0.5, 0.5])) evaluates two designs at once — this “vectorization” makes sampling studies fast.
Practical tip
Print .shape often. Most beginner errors in ML code are shape mismatches.
Notes: Where does this matter in engineering? Because heat_sink uses NumPy operations, it accepts arrays: heat_sink(np.array([1.0, 2.0]), np.array([0.5, 0.5])) evaluates two designs at once — this “vectorization” makes sampling studies fast. A practical tip: Print .shape often. Most beginner errors in ML code are shape mismatches.

## Slide 6: Pause and predict
Lesson 2 · Lists, arrays, functions, tables and plots · Predict before you look
If s has shape (6,) and you build X = np.column_stack([s, t]), what is X.shape?
Write down your answer, then continue to the next slide.
Notes: Time to predict. If s has shape (6,) and you build X = np.column_stack([s, t]), what is X.shape? Pause here and commit to an answer before moving on.

## Slide 7: What happens, and why
Lesson 2 · Lists, arrays, functions, tables and plots · Answer
Question: If s has shape (6,) and you build X = np.column_stack([s, t]), what is X.shape?
(6, 2): six samples (rows), two features (columns).
Notes: Here is the answer. (6, 2): six samples (rows), two features (columns).

## Slide 8: The data structures you will use
Lesson 2 · Lists, arrays, functions, tables and plots · Common misconception
Misconception
A 1-D array of shape (6,) is the same as a 2-D column of shape (6, 1).
What is actually true
They hold the same numbers but scikit-learn treats them differently. Features must be 2-D; use X = s.reshape(-1, 1) for one feature.
Takeaway Lists hold items; arrays do fast maths; DataFrames hold named tables; functions package reusable calculations. Check shapes.
Notes: A common misconception is this: A 1-D array of shape (6,) is the same as a 2-D column of shape (6, 1). In fact: They hold the same numbers but scikit-learn treats them differently. Features must be 2-D; use X = s.reshape(-1, 1) for one feature. The takeaway: Lists hold items; arrays do fast maths; DataFrames hold named tables; functions package reusable calculations. Check shapes.

## Slide 9: Key takeaways from this lesson
Summary
1
The data structures you will use
Lists hold items; arrays do fast maths; DataFrames hold named tables; functions package reusable calculations. Check shapes.
Notes: To sum up this lesson. The data structures you will use: Lists hold items; arrays do fast maths; DataFrames hold named tables; functions package reusable calculations. Check shapes.

## Slide 10: NumPy, pandas, matplotlib, scikit-learn — and reproducible seeds
UP NEXT · LESSON 2.3
Next in Module 2: Lesson 3. Mark this lesson complete in the course before continuing.
Notes: That completes Lesson 2 of Module 2: Lists, arrays, functions, tables and plots. Next comes Lesson 3: NumPy, pandas, matplotlib, scikit-learn — and reproducible seeds.