## Slide 1: Linear regression, residuals and least squares
MODULE 04 · LESSON 1 OF 3 · ≈ 10 MIN
Module 4: Your first regression model
Fitting a line by minimizing squared residuals
4.1
Notes: Welcome to Module 4, Lesson 1 of the self-paced course Machine Learning Fundamentals for Surrogate-Based Engineering Optimization: Linear regression, residuals and least squares. This lesson belongs to the module Your first regression model and takes about 10 minutes. In this lesson: Fitting a line by minimizing squared residuals.

## Slide 2: Fitting a line by minimizing squared residuals
Lesson 1 · Linear regression, residuals and least squares · Intuition
On a test bench, a heater dissipates power P into a heat sink and we measure the temperature rise ΔT. Physics suggests ΔT ≈ R P. Measurements scatter. Linear regression finds the line that best follows the points. Each vertical gap between a point and the line is a residual. Least squares chooses the line that makes the sum of squared residuals as small as possible.
Adjust intercept and slope; residuals (dashed red) and error metrics update; snap to the least-squares solution. (Interactive in the online course.)
Notes: Fitting a line by minimizing squared residuals. On a test bench, a heater dissipates power P into a heat sink and we measure the temperature rise ΔT. Physics suggests ΔT ≈ R P. Measurements scatter. Linear regression finds the line that best follows the points. Each vertical gap between a point and the line is a residual. Least squares chooses the line that makes the sum of squared residuals as small as possible. Look at the figure. Adjust intercept and slope; residuals (dashed red) and error metrics update; snap to the least-squares solution. Scatter of temperature rise versus heater power with a fitted line and vertical dashed residual segments. Sliders set intercept and slope; the readout shows SSE, MAE, RMSE, R² and the least-squares coefficients.

## Slide 3: Fitting a line by minimizing squared residuals
Lesson 1 · Linear regression, residuals and least squares · The mathematics (1/2)
ŷi = b0 + b1 xi, ei = yi − ŷi, SSE = Σ ei2
b1 = (Σ(xi − x̄)(yi − ȳ))/(Σ(xi − x̄)2), b0 = ȳ − b1x̄
Symbol | Meaning | Unit
x = P | heater power (feature) | W
y = ΔT | measured temperature rise (target) | K
b0 | intercept: predicted ΔT at P = 0 | K
b1 | slope: K per W, i.e. a thermal resistance | K/W
ei | residual | K
Notes: Now the mathematics. ŷ_i = b_0 + b_1 x_i, e_i = y_i − ŷ_i, SSE = Σ e_i^2 b_1 = (Σ(x_i − x̄)(y_i − ȳ))/(Σ(x_i − x̄)^2), b_0 = ȳ − b_1x̄ x = P is the heater power (feature), in W. y = ΔT is the measured temperature rise (target), in K. b_0 is the intercept: predicted ΔT at P = 0, in K. b_1 is the slope: K per W, i.e. a thermal resistance, in K/W. e_i is the residual, in K.

## Slide 4: Fitting a line by minimizing squared residuals
Lesson 1 · Linear regression, residuals and least squares · The mathematics (2/2)
These formulas come from setting ∂SSE/∂b0 = ∂SSE/∂b1 = 0. With many features, the same idea gives β̂ = arg min ‖y − Xβ‖², solved by linear algebra (QR factorization in this page’s demos).
Notes: Continuing. These formulas come from setting ∂SSE/∂b_0 = ∂SSE/∂b_1 = 0. With many features, the same idea gives β̂ = arg min ‖y − Xβ‖², solved by linear algebra (QR factorization in this page’s demos).

## Slide 5: Fitting a line by minimizing squared residuals
Lesson 1 · Linear regression, residuals and least squares · In engineering practice
Engineering application
The fitted slope estimates the thermal resistance of the tested sink in K/W; the intercept captures an offset (e.g., sensor bias or ambient drift) in K. The same least-squares machinery fits polynomial response surfaces in Module 8: “linear” refers to linearity in the coefficients, not in x.
Practical tip
Always plot the data with the fitted line and the residuals. Patterns in residuals (curvature, funnel shape) reveal model inadequacy that a single number hides.
Notes: Where does this matter in engineering? The fitted slope estimates the thermal resistance of the tested sink in K/W; the intercept captures an offset (e.g., sensor bias or ambient drift) in K. The same least-squares machinery fits polynomial response surfaces in Module 8: “linear” refers to linearity in the coefficients, not in x. A practical tip: Always plot the data with the fitted line and the residuals. Patterns in residuals (curvature, funnel shape) reveal model inadequacy that a single number hides.

## Slide 6: Pause and predict
Lesson 1 · Linear regression, residuals and least squares · Predict before you look
Points: (P, ΔT) = (10 W, 7 K), (20 W, 13 K), (30 W, 19 K). What are the least-squares b₁ and b₀?
Write down your answer, then continue to the next slide.
Notes: Time to predict. Points: (P, ΔT) = (10 W, 7 K), (20 W, 13 K), (30 W, 19 K). What are the least-squares b₁ and b₀? Pause here and commit to an answer before moving on.

## Slide 7: What happens, and why
Lesson 1 · Linear regression, residuals and least squares · Answer
Question: Points: (P, ΔT) = (10 W, 7 K), (20 W, 13 K), (30 W, 19 K). What are the least-squares b₁ and b₀?
The points are exactly collinear: b₁ = 6 K / 10 W = 0.6 K/W, b₀ = 7 − 0.6 × 10 = 1 K. All residuals are zero.
Notes: Here is the answer. The points are exactly collinear: b₁ = 6 K / 10 W = 0.6 K/W, b₀ = 7 − 0.6 × 10 = 1 K. All residuals are zero.

## Slide 8: Fitting a line by minimizing squared residuals
Lesson 1 · Linear regression, residuals and least squares · Common misconception
Misconception
Least squares minimizes the perpendicular distances to the line.
What is actually true
Ordinary least squares minimizes vertical distances (errors in y), assuming x is known accurately.
Takeaway Least squares picks coefficients minimizing Σ residual²; the slope of ΔT vs P is a resistance in K/W.
Notes: A common misconception is this: Least squares minimizes the perpendicular distances to the line. In fact: Ordinary least squares minimizes vertical distances (errors in y), assuming x is known accurately. The takeaway: Least squares picks coefficients minimizing Σ residual²; the slope of ΔT vs P is a resistance in K/W.

## Slide 9: Key takeaways from this lesson
Summary
1
Fitting a line by minimizing squared residuals
Least squares picks coefficients minimizing Σ residual²; the slope of ΔT vs P is a resistance in K/W.
Notes: To sum up this lesson. Fitting a line by minimizing squared residuals: Least squares picks coefficients minimizing Σ residual²; the slope of ΔT vs P is a resistance in K/W.

## Slide 10: Measuring error: MAE, RMSE and R²
UP NEXT · LESSON 4.2
Next in Module 4: Lesson 2. Mark this lesson complete in the course before continuing.
Notes: That completes Lesson 1 of Module 4: Linear regression, residuals and least squares. Next comes Lesson 2: Measuring error: MAE, RMSE and R².