## Slide 1: Noise versus limited knowledge, and a numerical example
MODULE 09 · LESSON 3 OF 3 · ≈ 12 MIN
Module 9: Gaussian processes and uncertainty
Two sources of uncertainty
9.3
Notes: Welcome to Module 9, Lesson 3 of the self-paced course Machine Learning Fundamentals for Surrogate-Based Engineering Optimization: Noise versus limited knowledge, and a numerical example. This lesson belongs to the module Gaussian processes and uncertainty and takes about 12 minutes. In this lesson: Two sources of uncertainty.

## Slide 2: Two sources of uncertainty
Lesson 3 · Noise versus limited knowledge, and a numerical example · Intuition
Aleatory uncertainty (observation noise): repeat the experiment and you get a different value. Epistemic uncertainty (limited knowledge): you have not observed the function there yet; more samples reduce it. Deterministic simulators have (essentially) no noise, so GP uncertainty is epistemic. Experiments have both. The nugget term σn² lets the GP stop chasing noise.
The same noisy data fitted with a near-zero nugget (forced interpolation) and with a noise term.
Notes: Two sources of uncertainty. Aleatory uncertainty (observation noise): repeat the experiment and you get a different value. Epistemic uncertainty (limited knowledge): you have not observed the function there yet; more samples reduce it. Deterministic simulators have (essentially) no noise, so GP uncertainty is epistemic. Experiments have both. The nugget term σ_n² lets the GP stop chasing noise. Look at the figure. The same noisy data fitted with a near-zero nugget (forced interpolation) and with a noise term. Two panels. Left: the GP mean passes through every noisy point, wiggling, with a narrow band at the points. Right: with a noise term, the mean is smoother and closer to the true curve and the band does not pinch to zero at the data.

## Slide 3: Two sources of uncertainty
Lesson 3 · Noise versus limited knowledge, and a numerical example · The mathematics (1/2)
Worked example (noise-free, zero prior mean, σf = 1, ℓ = 0.5). Observations: y(0) = 1, y(1) = 0. Predict at x* = 0.5.
Kernel between the observations: k(0,1) = exp(−1²/(2·0.5²)) = e−2 = 0.1353. So K = [[1, 0.1353], [0.1353, 1]].
Kernel to the query: k(0, 0.5) = k(1, 0.5) = exp(−0.25/0.5) = e−0.5 = 0.6065.
α = K−1y: det = 1 − 0.1353² = 0.9817; α = (1/det)·[1, −0.1353] = [1.0187, -0.1379].
Mean: μ(0.5) = 0.6065 × (1.0187 + (-0.1379)) = 0.5342.
Variance: σ² = 1 − k*TK−1k* = 1 − 2 × 0.6065² × (1 − 0.1353)/det = 0.3519, so σ = 0.5933.
Notes: Now the mathematics. Worked example (noise-free, zero prior mean, σ_f = 1, ℓ = 0.5). Observations: y(0) = 1, y(1) = 0. Predict at x* = 0.5. 1. Kernel between the observations: k(0,1) = exp(−1²/(2·0.5²)) = e^{−2} = 0.1353. So K = [[1, 0.1353], [0.1353, 1]]. 2. Kernel to the query: k(0, 0.5) = k(1, 0.5) = exp(−0.25/0.5) = e^{−0.5} = 0.6065. 3. α = K^{−1}y: det = 1 − 0.1353² = 0.9817; α = (1/det)·[1, −0.1353] = [1.0187, -0.1379]. 4. Mean: μ(0.5) = 0.6065 × (1.0187 + (-0.1379)) = 0.5342. 5. Variance: σ² = 1 − k_*^TK^{−1}k_* = 1 − 2 × 0.6065² × (1 − 0.1353)/det = 0.3519, so σ = 0.5933.

## Slide 4: Two sources of uncertainty
Lesson 3 · Noise versus limited knowledge, and a numerical example · The mathematics (2/2)
Interpretation: the GP mean is a covariance-weighted combination of the observations, μ(x*) = wTy with weights w = K−1k* = [0.5342, 0.5342]. By symmetry both observations get the same weight, but the weights are not required to sum to 1 (here they sum to 1.068), so the prediction is not an arithmetic average: μ(0.5) = 0.5342, slightly above 0.5. The weights depend on how strongly the query correlates with each observation (k*) and how the observations correlate with each other (K). Far from all data the weights shrink towards 0 and μ returns to the prior mean. The uncertainty here is substantial because ℓ is comparable to the spacing.
Notes: Continuing. Interpretation: the GP mean is a covariance-weighted combination of the observations, μ(x*) = w^Ty with weights w = K^{−1}k_* = [0.5342, 0.5342]. By symmetry both observations get the same weight, but the weights are not required to sum to 1 (here they sum to 1.068), so the prediction is not an arithmetic average: μ(0.5) = 0.5342, slightly above 0.5. The weights depend on how strongly the query correlates with each observation (k_*) and how the observations correlate with each other (K). Far from all data the weights shrink towards 0 and μ returns to the prior mean. The uncertainty here is substantial because ℓ is comparable to the spacing.

## Slide 5: Two sources of uncertainty
Lesson 3 · Noise versus limited knowledge, and a numerical example · In engineering practice
Engineering application
Noisy experiments (AM porosity, machining roughness): include a noise term and estimate it, ideally checked against repeat tests. Deterministic CFD: use a tiny nugget for numerical stability only — but note that CFD can show small “numerical noise” from meshing and convergence, which a small fitted nugget can absorb.
Practical tip
Report which uncertainty the GP represents (epistemic only, or including noise) and how hyperparameters were chosen. Uncertainty bands are model-dependent and are not guarantees.
Notes: Where does this matter in engineering? Noisy experiments (AM porosity, machining roughness): include a noise term and estimate it, ideally checked against repeat tests. Deterministic CFD: use a tiny nugget for numerical stability only — but note that CFD can show small “numerical noise” from meshing and convergence, which a small fitted nugget can absorb. A practical tip: Report which uncertainty the GP represents (epistemic only, or including noise) and how hyperparameters were chosen. Uncertainty bands are model-dependent and are not guarantees.

## Slide 6: Pause and predict
Lesson 3 · Noise versus limited knowledge, and a numerical example · Predict before you look
Single observation y(0) = 2 with zero prior mean, σf = 1, ℓ = 1, no noise. What is μ(1)?
Write down your answer, then continue to the next slide.
Notes: Time to predict. Single observation y(0) = 2 with zero prior mean, σ_f = 1, ℓ = 1, no noise. What is μ(1)? Pause here and commit to an answer before moving on.

## Slide 7: What happens, and why
Lesson 3 · Noise versus limited knowledge, and a numerical example · Answer
Question: Single observation y(0) = 2 with zero prior mean, σf = 1, ℓ = 1, no noise. What is μ(1)?
μ(1) = k(1,0)·y/k(0,0) = e−0.5 × 2 ≈ 1.213. The prediction decays toward the prior mean 0 with distance.
Notes: Here is the answer. μ(1) = k(1,0)·y/k(0,0) = e^{−0.5} × 2 ≈ 1.213. The prediction decays toward the prior mean 0 with distance.

## Slide 8: Two sources of uncertainty
Lesson 3 · Noise versus limited knowledge, and a numerical example · Common misconception
Misconception
A wider uncertainty band means the simulator is noisier there.
What is actually true
For deterministic simulators, the band reflects lack of data and model assumptions, not noise.
Takeaway Noise (aleatory) vs limited data (epistemic); GP bands reflect assumptions — verify and calibrate.
Notes: A common misconception is this: A wider uncertainty band means the simulator is noisier there. In fact: For deterministic simulators, the band reflects lack of data and model assumptions, not noise. The takeaway: Noise (aleatory) vs limited data (epistemic); GP bands reflect assumptions — verify and calibrate.

## Slide 9: Key takeaways from this lesson
Summary
1
Two sources of uncertainty
Noise (aleatory) vs limited data (epistemic); GP bands reflect assumptions — verify and calibrate.
Notes: To sum up this lesson. Two sources of uncertainty: Noise (aleatory) vs limited data (epistemic); GP bands reflect assumptions — verify and calibrate.

## Slide 10: Objectives, bounds, constraints; minimization and maximization
UP NEXT · LESSON 10.1
That completes Module 9. Before moving on, review the Module 9 flashcards and take its quiz in the course (pass mark 70%). Next: Module 10, Optimization foundations.
Notes: That completes Lesson 3 of Module 9: Noise versus limited knowledge, and a numerical example. This was the last lesson of the module, so review the flashcards and take the Module 9 quiz in the course. Next comes Module 10, Optimization foundations, starting with Objectives, bounds, constraints; minimization and maximization.